## Slide 1
SIGNALS AND SYSTEMS
FOURIER TRANSFORM
Applications in Signal Processing
Communication • Audio Processing• Images Processing
• Filtering • Spectrum Analysis
TIRTH SHAH
Enrolment: 12502060601060
Electronics & Communication Engineering
A.D. Patel Institute of Technology, CVM University
Faculty: Dr. Hitesh Shah • 22 October 2026
TIME DOMAIN → FREQUENCY DOMAIN
x(t)
X(ω): magnitude + phase

## Slide 2
Introduction to Fourier Transform
>> Fourier Transform is a mathematical tool used for frequency analysis of signals
LT → Math. tool → analysis of systems & ckts
>> Fourier Transform can exist for -
1) Energy signals → absolutely integrable ✓
2) Power signals → not absolutely integrable, but the FT exists by using Fourier transform properties
3) Impulse related signals → absolutely integrable
LT :-
1) ES
2) PS
3) NENP (only up to some extent)
>> Representation:
X(ω) in rad/sec, X(f) in Hz, ω = 2πf
>> Formulae:
FT pair
1) x(t) → X(jω)
FT
2) X(jω) → x(t)
IFT
>> Conversion of LT to FT:
LT
FT
01 • THE CORE IDEA
Notes: One-page version of the lecture notes.

## Slide 3
02 • APPLICATION IN COMMUNICATION
03
Finding frequencies in a communication signal
Fourier analysis shows where information is located in frequency and how much bandwidth it occupies.
MODULATION
A message changes a carrier. In AM, sidebands appear around the carrier frequency.
CHANNEL SELECTION
A band-pass filter keeps the desired radio band and rejects nearby stations or interference.
BANDWIDTH
The spectrum helps engineers avoid overlap between channels.
AM SPECTRUM EXAMPLE
95 kHz
100 kHz
105 kHz
For carrier fc = 100 kHz and message fm = 5 kHz:\nSidebands = fc ± fm = 95 kHz and 105 kHz.\nBandwidth = 2fm = 10 kHz.

## Slide 4
03 • APPLICATION IN AUDIO PROCESSING
04
Using the fourier transform to clean and shape sound
Audio contains bass, voice tones, treble and sometimes unwanted noise.
NOISE REDUCTION
A low-pass filter can reduce high-frequencies. A narrow notch filter can target a hum tone.

## Slide 5
04 • APPLICATION IN IMAGE PROCESSING
05
Images also contain spatial frequencies
Slow brightness changes are low spatial frequencies; fine texture and sharp edges are high spatial frequencies.
LOW-PASS → BLUR
Suppresses high spatial frequencies to smooth an image or reduce small-scale noise; fine details soften.
HIGH-PASS → SHARPEN
Emphasizes rapid intensity changes and edges. Too much enhancement can amplify noise.
FREQUENCY-DOMAIN WORKFLOW
IMAGE
pixels
TRANSFORM
frequency map
FILTER
keep/remove
INVERSE
filtered image
Apply a frequency mask, then transform back to the image domain.

## Slide 6
05 • FILTERING
06
Filters keep useful frequencies and reduce unwanted ones
In the frequency domain, filtering is represented by Y(ω) = X(ω)H(ω).
LOW-PASS
Passes low frequencies; reduces high-frequency noise. Example: smoothing audio or images.
HIGH-PASS
Passes high frequencies; highlights edges or rapid changes and can remove slow drift.
BAND-PASS
Passes only a selected range; useful for selecting a radio channel.
IDEAL FILTER RESPONSE (SCHEMATIC)
Frequency → cutoff →
A practical filter has a transition band rather than a perfectly vertical cutoff. Choose the filter based on the useful signal band and the noise to remove.

## Slide 7
06 • SPECTRUM ANALYSIS
07
A spectrum reveals the frequencies inside a signal
Plot frequency on the horizontal axis and magnitude on the vertical axis; peaks indicate dominant tones or harmonics.
PEAK LOCATION
Tells you which frequency is present.
PEAK HEIGHT
Shows relative strength of that frequency component.
FFT
Computes the Discrete Fourier Transform efficiently for sampled signals.
SQUARE WAVE: ODD HARMONICS
1
3
5
7
9
An ideal square wave contains odd harmonics:\nx(t) = (4A/π)[sin(ω₀t) + ⅓sin(3ω₀t) + ⅕sin(5ω₀t) + …]\nThe amplitudes fall approximately as 1/n.

## Slide 8
07 • SOLVED EXAMPLE
09
AM: calculate the sidebands and bandwidth
Given carrier fc = 100 kHz and message fm = 5 kHz.
Step 1: Multiply message and carrier: s(t)=cos(ωmt)cos(ωct).
Step 2: Use cos A cos B = ½[cos(A+B)+cos(A−B)].
So the two components are at fc + fm and fc − fm.
Upper sideband = 100 + 5 = 105 kHz
Lower sideband = 100 − 5 = 95 kHz
Bandwidth = 105 − 95 = 10 kHz = 2fm
Interpretation: the message creates two sidebands around the carrier frequency.

## Slide 9
08 • SUMMARY & REFERENCES
10
One transform, five major applications
COMMUNICATION
Modulation, sidebands, channel selection and bandwidth.
AUDIO
Noise reduction, equalization and tone detection.
IMAGE PROCESSING
Blurring, sharpening and transform-based compression.
FILTERING
Keep the useful frequency band and suppress unwanted components.
SPECTRUM ANALYSIS
Find dominant frequencies and harmonics; FFT speeds digital analysis.
KEY IDEA
Magnitude shows strength; phase also matters when reconstructing signals.
Sampling reminder: for a band-limited signal, ideal sampling requires fs > 2fmax; practical systems use anti-alias filters.
References: Oppenheim et al., Signals and Systems; Haykin & Van Veen, Signals and Systems; Gonzalez & Woods, Digital Image Processing; Cooley & Tukey (1965).
Thank you • Questions?